Concurrent Programming I
HPPS
David Marchant
Based on slides by:
Troels Henriksen, Randal E. Bryant and David R. O’Hallaron

---
Concurrent Programming
So far we’ve talked about threads and processes each running a complete programme
Each programme has been sequential in nature
We can spread processing over several threads or processes, each part of the same programme
Twice the resources means twice the speed! (Nope)

---
The Basic Idea
We can break our processing over several workers
Many hands make light work
Single process
Runs for 10 mins
Two processes
Each run for 5 mins

---
Logical View of Threads
Threads associated with process form a pool of peers
Each thread can be processed in parallel
Threads associated with process foo
T2
T4
T1
shared code, data
and kernel context
T3
T5

---
Concurrent Threads
Two threads are concurrent if their flows overlap in time
Otherwise, they are sequential
Examples:
Concurrent: A & B, A&C
Sequential: B & C
Thread A
Thread B
Thread C
Time

---
Concurrent and Parallel Threads
Single Core Processor
Simulate parallelism by time slicing
Multi-Core Processor
Can have true parallelism
Thread A
Thread B
Thread C
Thread A
Thread B
Thread C
Time
Run 3 threads on 2 cores

---
Parallel Systems are the default
For many years now mulit-core systems have been standard
If we paid for 8 cores, we want to use them!
...and not just on running background processes with slightly fewer context switches, we want a single programme to use the all of the hardware

---
Parallelism is about speed.
How do we quantify whether parallelisation made a program faster, and by how much?
How can we estimate the potential benefit of parallelising a program?
Are there limits to the potential gains of parallelism?So far we’ve talked about threads and processes each running a complete programme

---
Latency
Often called runtime
How long it takes for a program to run on some workload.
Both difficult and easy to measure
Wall time is the time it takes in the real world.
CPU time is the total amount of time spent executing code counting all processors.
Two processes
Each run for 5 mins
Single process
Runs for 10 mins
Here the CPU time is the same,
But the wall time has halved

---
Latency
Suppose we have two programmes, P1 and P2 that each perform the same task, and take T1 and T2 respectively:
Speedup greater than one means P2 is faster than P1 , else it is slower.
P1 and P2 must solve the same problem for their latencies to be comparable.
HINT: This is a good metric to include in any reportorting on your own programmes
Latency=
T1
T2

---
Throughput
Sometimes latency is inappropriate—what is the running time of a potentially-infinite web server?
Can measure latency for individual requests, but is that really useful?
E.g. web requests served per second, or number of bytes processed per clock cycle.
Using throughput we can compare programs that have different workloads.
Throughput=
Workload
Time

---
Speedup in Throughput
Suppose we have two programmes, P1 and P2 that each perform the same task, and have a throughput of Q1 and Q2 respectively:
Speedup greater than one means P2 is faster than P1 , else it is slower.
P1 and P2 must solve the same problem for their throughputs to be comparable.
HINT: This is another good metric to include in any reportorting on your own programmes
Q1
Throughput Speedup =
Q2

---
Scalability
Basically how well our system improves (or not) as we make it bigger
Both are similar, but we are altering different parameters in our system
How the system improves in its capacity (runtime or throughput) as we add more resources, such as more processors
How the system throughput changes as we add more workload

---
Scalability Example
Rendering Mandelbrot fractals
Each pixel can be computed
independently
The image size corresponds to
the workload
Regarding parallelism, there are
two sorts of scalability that we are
interested in.

---
Strong Scaling
How the runtime varies with the number of processors for a fixed problem size.
This shows sub-linear strong scalability—8 threads barely gets us 4 × speedup
Speedup graph for rendering a 104 pixel Mandelbrot fractal as we use more threads:

---
Weak Scaling
How the runtime varies with the number of processors for a fixed problem size relative to the number of processors.
Pretty decent weak scalability! By far more common than strong scalability.
Speedup graph for rendering a Mandelbrot fractal with 104 pixels per thread:

---
How do we estimate the potential benefits of parallelising a program, without just implementing it and measuring how well it goes?

---
Amdahl’s Law
If p is the proportion of execution time that benefits from parallelisation, then S(N) is maximum theoretical speedup achievable by execution on N processors, and is given by:
Why is can p not equal 1?
Reading, writing and other fundamentally sequential parts mean p will never be 1 in practice
1
p
S(N) =
(1-p) +
N

---
Amdahl’s Law

---
Amdahl’s Law
Amdahl’s Law predicts strong scalability.
For a fixed problem size, there will always come a point of diminishing returns.
Makes parallelisation seem pointless…
You have a simulation that runs in 1 hour.
Then you get a computer that is ten times faster.
Usually you don’t decide to run the simulation in six minutes, instead you make a simulation that is ten times as precise and still runs in 1 hour.
Consider weather forecasting...
Bigger machines let us solve bigger problems in the same time!
But...

---
Gustadson’s Law
If s is the proportion of execution time that must be sequential, then S(N) is maximum theoretical speedup achievable by execution on N processors, and is given by:
Assumes that parallel workload increases just as fast as number of processors.
Predicts weak scalability.
In practice often more relevant than Amdahl’s Law.
S(N) = N + (1-N) x s

---
Gustadson’s Law

---
The Fine Print
Both Amdahl’s and Gustafson’s Laws are idealised abstractions and ignore important real-world concerns:
Locality.
Communication.
Synchronisation.
But they are still a good theoretical framework for estimating the value of parallelising some program.

---
How do we start throwing threads at our problems?

---
Parallel Loops
For scientific computing, we are mostly concerned with parallelising straightforward loops such as this matrix multiplcation code
Iterations of the outer two loops are independent.
Can be computed by different threads.
void matmul(int n , const double ∗x ,
        const double ∗y , double ∗out ) {
for ( int i = 0 ; i < n ; i++) {
for ( int j = 0 ; j < n ; j++) {
out [ i ∗n+j ] = 0 ;
for ( int l = 0 ; l < n ; l++) {
out [ i ∗n+j ] += x [ i ∗n+j ] ∗ y [ i ∗n+j ] ;
}
}
}
}

---
Simplest OpenMP Example
Directives used to indicate how run C program in parallel.
Clauses (covered later) can be used to customise the behaviour.
Semantics are the sequential elision—how the program would behave if we ignored the directives.
We are only scratching the surface of OpenMP in this course!
#pragma omp parallel for
for (int i = 0 ; i < n ; i++) {
A[i] = A[i] * 2;
}

---
Simplest OpenMP Example
print (“Program Starts\n”);
n = 1000;
#pragma omp parallel for
for (int i=0; i<n; i++) {
A[i] = B[i] + C[i];
}
m = 500;
#pragma omp parallel for
for (int j=0; j<m; j++) {
p[j] = q[j] - r[j];
}
print (“Program Ends\n”);
exit(0),
Sequential
Parallel
Sequential
Parallel
Sequential
Program starts sequential.
Parallel regions split across multiple threads.
Parallel region ends when all threads done.
Worker threads kept running in background.

---
Compilation
#include <stdio.h>
#include <stdlib.h>
int main (void) {
int n = 100000000;
int ∗arr = malloc (n∗sizeof(int)) ;
#pragma omp parallel for
for (int i=0; i<n; i++) {
arr[ i ] = i ;
}
free(arr);
}
$ gcc -o openmp-example openmp-example.c -fopenmp

---
Controlling the number of threads
$ time OMP_NUM_THREADS=1 ./openmp-example
real	0m0.124s
user	0m0.034s
sys	0m0.090s
$ time OMP_NUM_THREADS=2 ./openmp-example
real	0m0.076s
user	0m0.033s
sys	0m0.104s
$ time OMP_NUM_THREADS=3 ./openmp-example
real	0m0.054s
user	0m0.039s
sys	0m0.133s
$ time OMP_NUM_THREADS=4 ./openmp-example
real	0m0.046s
user	0m0.054s
sys	0m0.184s
Wall time
CPU time (user)
CPU time (system)
Wall time
CPU time (user)
CPU time (system)
Wall time
CPU time (user)
CPU time (system)
Wall time
CPU time (user)
CPU time (system)

---
Memory model
Variables declared inside a loop iteration are private.
Variables declared outside are shared.
Be extremely careful when modifying shared variables—OpenMP will not protect you!
This is known as a race condition, multiple threads are reading and writing to the same location. Who gets there first? We don’t know!
We will cover this in more depth next week
Main
sum
0
Double sum=0;
#pragma omp parallel for
for (int i = 0 ; i < n ; i++) {
sum += A[i];
}
Thread 1
Thread 2
sum
0
sum
0
sum
1
sum
1
sum
?

---
Reductions
Instead of doing a summation sequentially
we can do it like:
and have one compute the left part, and a second one compute the right, combining their results at the end.
(((((((x0 + x1) + x2) + x3) + x4) + x5) + x6) + x7)
(x0 + x1 + x2 + x3) + (x4 + x5 + x6 + x7)
Is this valid?

---
Reductions
Instead of doing a summation sequentially
we can do it like:
and have one compute the left part, and a second one compute the right, combining their results at the end.
(((((((x0 ⊕ x1) ⊕ x2) ⊕ x3) ⊕ x4) ⊕ x5) ⊕ x6) ⊕ x7)
(x0 ⊕ x1 ⊕ x2 ⊕ x3) ⊕ (x4 ⊕ x5 ⊕ x6 ⊕ x7)
What about now?

---
Reductions
A binary operator ⊕ : α → α → α is said to be commutative if
It is associative if
We can do a parallel “sum” with any associative operator, called a reduction.
For convenience, we also tend to require a neutral element 0⊕:
x ⊕ y = y ⊕ x
x ⊕ (y ⊕ z) = (x ⊕ y) ⊕ z
x ⊕ 0⊕ = 0⊕ ⊕ x = x

---
Reduction example
double dotprod (int n, double ∗x, double ∗y) {
double sum = 0 ;
#pragma omp parallel for reduction (+: sum)
for (int i=0; i<n; i++) {
sum += x[i] ∗ y[i] ;
}
return sum ;
}
Must initialise accumulator variable to neutral element.
Must explicitly tell OpenMP the combining operator (+, ∗, −, &&, || , &, |, ^, max, or min).

---
Parallelising Matrix Multiplication
void matmul_seq(int n , const double ∗x ,
  const double ∗y, double ∗out) {
for (int i=0; i<n; i++) {
for (int j=0; j<n; j++) {
double acc = 0;
for (int l=0; l<n; l++) {
acc += x[i∗n+l] ∗ y[j∗n+l] ;
}
out[i∗n+j] = acc;
}
}
}
Runtime for n=1000: 0.87s.
Three nested loops.
Which do we parallelise, and how?

---
Parallelising Matrix Multiplication
void matmul_seq(int n , const double ∗x ,
  const double ∗y, double ∗out) {
#pragma omp parallel for
for (int i=0; i<n; i++) {
for (int j=0; j<n; j++) {
double acc = 0;
for (int l=0; l<n; l++) {
acc += x[i∗n+l] ∗ y[j∗n+l] ;
}
out[i∗n+j] = acc;
}
}
}
Runtime: 0.059s (was. 0.87s seq) — pretty good for adding one line of code!
But this only parallelises across the rows of the result matrix.

---
Parallelising Matrix Multiplication
void matmul_seq(int n , const double ∗x ,
  const double ∗y, double ∗out) {
#pragma omp parallel for collapse(2)
for (int i=0; i<n; i++) {
for (int j=0; j<n; j++) {
double acc = 0;
for (int l=0; l<n; l++) {
acc += x[i∗n+l] ∗ y[j∗n+l] ;
}
out[i∗n+j] = acc;
}
}
}
collapse(2) clause combines loops to one parallel n*n iteration loop,
Runtime: 0.055s (was 0.059s without collapse) — not much impact here.
Would matter more if we had fewer iterations in outer loop.

---
Parallelising Matrix Multiplication
void matmul_seq(int n , const double ∗x ,
  const double ∗y, double ∗out) {
for (int i=0; i<n; i++) {
for (int j=0; j<n; j++) {
double acc = 0;
#pragma omp parallel for reduction(+:acc)
for (int l=0; l<n; l++) {
acc += x[i∗n+l] ∗ y[j∗n+l] ;
}
out[i∗n+j] = acc;
}
}
}
Runtime: 3.95s (vs. 0.87s sequential)—this sucks.
Almost always better to parallelise outermost loops.

---
Scheduling Clauses
By default, OpenMP splits the iterations of a parallel loop evenly among the threads (static scheduling). This is not always optimal.
int fib (int n) {
if (n <= 1) {
return 1;
} else {
return fib(n−1) + fib(n−2);
}
}
Consider a loop that computes fib(i) for each i<n.
Since time to compute fib(i) is over twice that of fib(i-1), the threads with the early iterations finish much faster than the threads with the later iterations.
#pragma omp parallel for schedule(static)
for (int i=0; i<n; i++) {
fibs[i] = fib(i);
}

---
Dynamic Scheduling
Dynamic scheduling assigns each thread an iteration, and is given more iterations when it finishes.
No idle threads (as long as there are unclaimed iterations to run).
#pragma omp parallel for schedule(dynamic)
for (int i=0; i<n; i++) {
fibs[i] = fib(i);
}
On my machine static ran in 5.2s, where dynamic ran in 2.27s—much better!
By default, assigns single iterations at a time, which is slow for very large loops with quick iterations.
Use schedule(dynamic,K) to schedule K iterations at a time to threads.

---
Summary
Parallelism is about speedup.
Describe performance differences with speedup.
Latency for programs that compute the same thing.
Throughput if not.
Strong scaling is solving the same problem faster.
Weak scaling is solving a bigger problem in the same time.
OpenMP is a simple language extension for parallelising loops in C programs.
Use #pragma omp parallel for to parallelise a for-loop.
Generally parallelising the outer most loop works best